## Slide 1
FloodView
PS 26161 · NTRO
HOW THE SYSTEM IS BUILT
Four layers. Each one does a single job and hands its result to the next.
SMART INDIA
HACKATHON 2026
Anyone can run it from a browser. Everything underneath is free, open and cached for offline use.
1
LAYER 1 · WHAT USERS SEE
Interactive Dashboard
Opens in any browser. Maps, charts, 3D globe, download buttons.
Command Line
For batch runs and automation. One instruction, full report.
LAYER 2 · THE BRAIN THAT COORDINATES EVERYTHING
Central Coordinator
Takes the request, checks the inputs are sensible, starts the work, hands back the answer.
Background Worker
Runs the heavy calculation on its own so the dashboard never freezes — it answers in 0.21 s.
No coding needed. A dam safety officer picks a dam and presses one button.
Like a front desk plus a workshop: the desk answers instantly, the work happens out back.
LAYER 3 · THE SIMULATION ENGINE — where the flood is actually modelled
Dam Break Model
How the wall gives way: breach width, how fast it opens, peak water released. From published dam-safety research, not guesswork.
Flood Spread Calculator
Follows the water across the land second by second at 30-metre detail. Slows it through forest, speeds it over concrete. Adjusts its own step size to stay stable.
Uncertainty Analysis
Runs 30 variations with different breach sizes. Reports best case, worst case and most likely — never one false number.
Near-Dam 3D Physics
Violent water right at the wall: overtopping, splashing. Covers about 600 m for 15 s. Adds detail; it does not replace the main model.
Independent Cross-Check
The same textbook case run through Delft3D FM, a real Deltares kernel. Both engines land within 3 cm of each other. Proof, not a claim.
one-way
Terrain Preparation
Downloads satellite ground-height data, stitches the tiles together, cleans the artefacts, finds the dam wall, and maps what covers the land — forest, town, farmland — because that sets how fast water runs.
Flood Impact Assessment
Turns depth into consequence: ankle-deep, waist-deep, two to five metres, above five metres. Estimates buildings exposed and people at risk using published government formulas.
Quality Gates
Four mandatory checks run before any result is released. Still water stays still. No water is lost. No impossible depths. Answers match the textbook case. Fail any one and the result is blocked outright.
Report & Map Generator
Flood maps that open in standard mapping software, Google Earth overlays, inundation boundaries, time-lapse animations and spreadsheets — all geographically referenced at 30-metre detail.
LAYER 4 · DATA SOURCES — every one free, open and legal to redistribute
Satellite Ground Height
European Space Agency, 30-metre detail, worldwide, stored once and reused.
India's Dam Register
The government list of 5,000-plus large dams with height, storage and river.
Satellite Flood Imagery
Radar flood detection plus population density. Rejected automatically if too poor.
Land Cover Map
Forest, city or farmland at 10-metre detail — this decides how fast the water travels.
Pre-loaded Dam Profiles
Tehri at 260 m and 3,540 MCM, Khadakwasla at 33 m, plus their downstream towns.
Offline Cache
Fetched once, then held on disk. Demo day needs no network at all.
No commercial licence, no field survey, no specialist — total data cost is zero.

## Slide 2
FloodView
PS 26161 · NTRO
HOW IT WORKS — STEP BY STEP
From four simple inputs to a complete flood risk report, in minutes rather than weeks.
SMART INDIA
HACKATHON 2026
Seven steps. The officer performs step one. The system performs the other six.
2
Built-in uncertainty, not a single guess
▪ Thirty variations run with different breach sizes
▪ Reports the fifth and ninety-fifth percentile arrival band
▪ Best case, worst case and most likely — stated together
▪ This is how real engineering reports risk
Checked against an independent engine
▪ The same textbook case run through Delft3D FM as well
▪ A real Deltares kernel, not a lookalike of our own
▪ Our answer 0.0317 m error, theirs 0.0349 m
▪ The two engines agree to within 0.0294 m
Why the speed matters
▪ Today: weeks of specialist setup and licensed software
▪ Today: field survey costs before a single map exists
▪ FloodView: four inputs, free data, a full run in 47 seconds
▪ Any trained officer can run it — and it runs offline
Pick a Dam
Choose from the list, or type in position, height and storage. Four numbers, nothing more.
1
No specialist needed — the numbers are public.
Get the Terrain
Satellite ground-height data arrives at 30-metre detail and is cached for offline reuse.
2
Like fetching a 3D photograph of the valley.
Prepare the Land
Smooth the artefacts, locate the dam wall, and label what covers the ground downstream.
3
Forest slows water down; concrete speeds it up.
Model the Break
Work out how wide the breach grows, how quickly, and how much water is released at the peak.
4
Formulas drawn from decades of dam-safety study.
Simulate the Flood
Follow the water downstream second by second across the whole landscape — the core calculation.
5
The heavy step, and still only tens of seconds.
Assess the Impact
Which areas flood, how deep, when the water arrives, and how many people are exposed.
6
Depth becomes consequence, in plain numbers.
Publish Results
Maps, Google Earth overlays, charts and downloadable reports, ready for the people who decide.
7
One run produces the whole package.
WHAT COMES OUT AT THE END
Arrival Time Map
When the water reaches each town — the number that decides an evacuation order.
Inundation Envelope
The outer boundary of the flood, with a fifth-to-ninety-fifth percentile band around it.
Depth and Hazard Bands
Four hazard classes, from ankle-deep through to above five metres.
People and Buildings Exposed
Counts drawn from satellite population and building data, with the source stated.
Evidence Pack
The quality-gate results and the independent cross-check, attached to every single run.

## Slide 3
FloodView
PS 26161 · NTRO
USER JOURNEY — WHO DOES WHAT
Four lanes. The officer clicks; everything to the right of that happens on its own.
SMART INDIA
HACKATHON 2026
The person operating the system makes five decisions. The system takes roughly twenty thousand.
3
THE OFFICER
A dam-safety or disaster-management officer. No coding background.
THE COORDINATOR
Receives the request, checks it, and decides what work to start.
THE ENGINE
Does the mathematics: breach, flood spread, impact.
THE REPORTER
Turns results into maps, charts and files people can act on.
Opens the dashboard in a browser
Nothing to install.
Answers in under a fifth of a second
Even mid-run.
Idle, waiting for work
Shows the run picker
Any past run loads instantly.
Picks a dam — say Tehri, 260 m
Or types four numbers.
Checks the inputs are physically sensible
Rejects nonsense early.
Loads terrain, or fetches it once
yes → straight through · no → fetched once, then kept
Draws the study area on the map
Confirms before running.
Keeps the defaults, presses Run
One button.
Starts a separate worker for the heavy part
The page stays alive.
Models the breach, then the flood spread
Thirty variations.
Streams live progress, member by member
Never a frozen bar.
Watches the arrival times appear
Town by town.
Saves each result as it lands
Nothing is lost on a crash.
Scores impact: depth, hazard, people exposed
Published formulas.
Plots the flood on a 2D map and a 3D globe
Both stay loaded.
Downloads the pack for the district authority
Ready to circulate.
Attaches the quality-gate evidence
Every run, no exceptions.
Optionally runs the near-dam 3D detail
About 600 m, 15 s.
Exports maps, overlays, charts, spreadsheets
Standard formats.
Terrain already here?

## Slide 4
FloodView
PS 26161 · NTRO
WHAT IT IS BUILT WITH
Every piece is open-source and free to use. Nothing here carries a licence fee.
SMART INDIA
HACKATHON 2026
Total software licence cost: zero. Total field-survey cost: zero.
4
FLOOD SIMULATION
The mathematics that moves the water
NumPy and SciPy
the numerical core
Numba
compiles the hot loops, roughly 100x
PySPH
particle physics near the dam
Matplotlib
scientific plotting
Delft3D FM
Deltares kernel, 2026.01 build
MAPS AND GEOGRAPHY
Reads satellite data, writes map files
Rasterio
reads satellite ground-height data
GeoPandas
geographic boundaries and joins
Shapely
flood-zone shapes
PyProj
converts between coordinate systems
xarray
time-series flood data
Earth Engine
radar flood and population layers
SERVER AND API
Coordinates the work, never blocks the page
FastAPI
the web service
Uvicorn
runs it
Pydantic
validates every input
SQLite
keeps the run history
Celery
optional distributed worker
WHAT PEOPLE SEE
Maps, globe and charts in the browser
React
the interface
Vite
instant reloads while building
Leaflet
the 2D flood map
CesiumJS
the 3D globe with real terrain
Recharts
arrival-time and depth charts
ParaView
cinematic flood animation
PACKAGE AND PROVE
Ships anywhere, tests every change
Docker
the whole system, one command
Pytest
the automated test suite
Ruff
keeps the code clean
GitHub Actions
re-runs the gates on every change
The one line item a conventional study cannot avoid — the licensed modelling package — simply has no equivalent on this slide.
WHERE THE DATA COMES FROM — free, open, and cached so demo day needs no network
Copernicus Ground Height
European Space Agency · 30-metre detail
Earth Engine Imagery
Radar flood extent and population density
ESA Land Cover
Forest, town or farmland at 10 metres
Delft3D FM
Deltares, Netherlands · independent check
CWC Dam Register
The official Indian list, 5,000-plus dams
Local Cache
Fetched once, then offline

## Slide 5
FloodView
PS 26161 · NTRO
WHO USES IT, AND WHAT FOR
Four kinds of user inside the country, four data services outside it, twelve things the system does.
SMART INDIA
HACKATHON 2026
One system, four audiences: the operator, the emergency planner, the researcher and the policy maker.
5
Dam Safety Officer
Central Water Commission · watches dam health
Emergency Manager
District and national authority · plans the evacuation
Researcher / Engineer
Validates the model, runs comparative studies
Policy Maker
State or centre · decides where the safety budget goes
EVERYTHING INSIDE THIS BOX IS FLOODVIEW
Choose a dam and set the failure scenario
Run a full flood simulation — minutes, not weeks
Run thirty what-if variations for an honest range
Read the flood on a 2D map and on a 3D globe
Download the pack for the district authority
Get arrival times for every downstream town
Check answers against the known exact solution
Cross-check against the independent Delft3D engine
Estimate the population exposed, from satellite data
Estimate damage to buildings and to life
Run the detailed 3D physics right at the wall
Rank several dams against each other by priority
Copernicus Ground Height
30-metre satellite elevation
Earth Engine
Radar flood extent, population
Delft3D FM
Independent verification engine
CWC Dam Register
Official Indian dam records
Outside services are read, never written to. Nothing leaves the machine the system runs on.

## Slide 6
FloodView
PS 26161 · NTRO
WHAT EACH PART DOES
Six working parts and three supporting ones. Arrows show which way information travels.
SMART INDIA
HACKATHON 2026
Each part depends only on the parts to its left, so any one of them can be replaced on its own.
6
FLOODVIEW · THE WHOLE SYSTEM
Flood Simulation Engine
The mathematical core. Follows the water across the terrain step by step, using equations settled in hydraulic engineering.
The stepping loop, timestep by timestep
Flood-front tracking — where the water actually goes
Wet-and-dry handling at the flood edge
Runs across every processor core available
Terrain and Dam Break
Prepares the digital landscape, then models how the wall gives way — how wide, how quickly, how much water is released.
Terrain smoothing and artefact cleaning
Breach growth from published dam-safety work
Study-area definition around the dam
Ground cover mapped to how fast water flows
Impact and Risk
Turns depth into consequence: which areas, how deep, how many people, and what it is likely to cost.
Four hazard classes, ankle-deep to above five metres
Building damage from published damage curves
Loss-of-life estimates from the standard tables
Population exposed, read from satellite data
Near-Dam 3D Physics
Optional detail for the violent water right at the wall. It adds resolution; it never replaces the main simulation.
Hand-off from the flood solver, one direction only
A 3D domain roughly 600 metres across
Particle-based water, about 15 seconds of it
Overtopping and splash behaviour at the crest
Quality Assurance
Automated proof that must pass before a result is released. Four checks. Fail one and nothing is published.
Still water must stay still
No water may be created or lost
No impossible depths anywhere in the grid
The answer must match the independent engine
Reports and Maps
Everything a decision maker actually receives.
Flood depth maps for standard mapping tools
Boundary shapes for planning software
Google Earth overlays
Time-lapse animation frames
Spreadsheets of arrival times
The one rule the whole map obeys
A part may only depend on the parts to its left. That is why the near-dam 3D physics can be switched off entirely without touching anything else, and why the reporting stage can be rewritten without going near the mathematics. It is also what keeps each part testable on its own.
Supporting services
Settings Loader
Reads the run settings and checks them before anything starts
Dam Profile Library
Tehri, Khadakwasla and their downstream towns, ready to run
Offline Cache
Holds everything downloaded so the next run needs no network

## Slide 7
FloodView
PS 26161 · NTRO
FROM RAW DATA TO A DECISION
Three stages. Collect once, simulate on demand, then publish something a district officer can act on.
SMART INDIA
HACKATHON 2026
Stage one happens once per dam. Stages two and three happen every time somebody asks a question.
7
STAGE 1 · COLLECT AND PREPARE
Runs once per dam, then never again — the results are cached on disk.
Fetch the Terrain
Satellite ground-height tiles at 30-metre detail, free from the European Space Agency.
Stitch and Clean
Several tiles merged into one seamless surface, with cliff and water-body artefacts removed.
Label the Ground
Forest, town or farmland — this is what sets how much the land slows the water down.
Define the Study Area
Draw the box around the dam, in metres rather than degrees, on an even calculation grid.
Locate the Wall
Pin down exactly where the dam sits and where the breach would open. Everything keys off this.
terrain grid + breach position + ground-roughness map → handed to the simulation
STAGE 2 · SIMULATE
The whole of this stage completes in about 47 seconds for a full Tehri run.
Model the Failure
Breach width, how fast it opens, and the peak water released. Thirty variations, not one.
Spread the Water
Every cell of the landscape, second by second, downstream. The core of the whole system.
Sweep the Uncertainty
Different breach sizes give different outcomes. The answer is a band, not a point.
Time the Arrivals
When does the water reach each town? This is the number an evacuation order depends on.
Optional 3D Detail
Violent water at the wall itself. About 600 metres, 15 seconds. It can never reach a town.
maximum depth + arrival time + the percentile band → handed to the reporting stage
STAGE 3 · PUBLISH
Nothing reaches this stage until all four quality gates have passed.
Score the Impact
How deep in each area, how many people exposed, and the likely damage — with the source stated.
Draw the Flood Maps
Colour-coded depth maps that open in any standard mapping tool, plus Google Earth overlays.
Render the Animation
Time-lapse of the flood spreading, for briefings and for public awareness material.
Fill the Dashboard
Maps, globe, charts, gauge traces and every download, live in the browser. Nothing to install.
Attach the Evidence
The four gate results and the independent cross-check travel with the report, every time.
The one-way arrow matters. The near-dam 3D physics reads the flood solver's output and refines it. It never feeds back. Anyone claiming a two-way coupling here would be overstating what was built.
Stage one is the reason this works offline. Once a dam's terrain has been fetched, the entire pipeline runs with the network unplugged — which is the assumption demo day is built on.

## Slide 8
FloodView
PS 26161 · NTRO
WHY IT MATTERS
India has more than five thousand large dams, many of them ageing. Today only a handful ever get studied.
SMART INDIA
HACKATHON 2026
The point is not a better flood model. The point is that every dam can be screened, not just the funded ones.
8
A conventional dam-break study takes weeks of specialist time and licensed software, so it is only commissioned for the dams somebody has already worried about.
FloodView completes the same screening in minutes, from free satellite data — which changes who gets screened, not just how fast.
SAVES LIVES
▪ Arrival times per town — the number that sets an evacuation order
▪ Flood extent showing which areas to clear, and in what order
▪ Population exposed, estimated from satellite data
▪ Works with the network unplugged, when it matters most
SAVES MONEY
▪ No software licence to buy — every component is open
▪ No field survey needed before the first map exists
▪ Minutes per dam instead of weeks
▪ Run by a trained officer, not a hired specialist
HONEST BY DESIGN
▪ Reports a range, never a single falsely precise number
▪ Poor satellite imagery is refused, not quietly used
▪ Four quality gates block a bad result rather than flagging it
▪ Every limitation is stated on the report itself
INDEPENDENTLY CHECKED
▪ Matched against Delft3D FM on the same textbook case
▪ Our error 0.0317 m, theirs 0.0349 m
▪ Both engines agree to within 0.0294 m
▪ Built on two decades of published dam-safety research
How that compares with current practice
What you need
How it is done today
How FloodView does it
Time to a first answer
Weeks of specialist setup
Minutes — pick a dam and press run
Data you must buy
Licensed elevation data plus a field survey
None. Free satellite data, cached locally
Independent verification
Rarely available, rarely published
Cross-checked against Delft3D FM, published here
How uncertainty is shown
A single number, with no band around it
Thirty runs — best, worst and most likely
Poor satellite imagery
Used anyway, because there is nothing else
Refused automatically below the quality threshold
Network on the day
Required — the tools are cloud-hosted
Not required. Everything runs from cache
Refusing a bad input is a feature, not a gap. At Khadakwasla the radar scene scored 0.486 against a 0.5 threshold and was rejected outright — no substitute overlay was drawn in its place.
None of the right-hand column is aspiration. Every row in it is running today, on the machine this deck was built on, and the numbers quoted came off that machine.

## Slide 9
FloodView
PS 26161 · NTRO
HOW WE KNOW THE ANSWERS ARE RIGHT
Four checks that must pass, plus a comparison against an engine we did not write.
SMART INDIA
HACKATHON 2026
If a check fails, the result is blocked — not flagged, not footnoted. Blocked.
9
No result is ever shown until all four checks pass. A warning label on a wrong flood map is worse than no map at all, so a failed check stops the run.
CHECK 1 · STILL WATER STAYS STILL
Water in a bowl with nothing pushing it must not drift.
Measured drift: 0.0000000000000598 metres per second.
The threshold allows a thousand times more than that.
Result: passes, with room to spare.
CHECK 2 · NO WATER APPEARS OR VANISHES
Total water in the simulation must stay constant.
Measured loss across a thousand steps: 0.000000 per cent.
Exact to the limit of what the machine can represent.
Result: passes.
CHECK 3 · NO IMPOSSIBLE NUMBERS
Depth can never be negative, and nothing may go undefined.
The flood edge, where water meets dry ground, is the hard part.
Every cell across every test case stayed physical.
Result: passes on all cases.
CHECK 4 · MATCHES THE KNOWN ANSWER
A textbook dam-break has an exact answer written in 1892.
Exact depth at the wall: 4.444 metres.
Our answer: 4.532 metres — an error of about 3 centimetres.
Result: passes, well inside tolerance.
And then checked against an engine we did not write
What was actually done
▪ The same textbook case was run twice — once through our engine, once through Delft3D FM.
▪ Delft3D FM is made by Deltares, an independent Dutch institute. Governments use it for real flood studies.
▪ It is a genuine Deltares kernel running here, 2026.01 build — not a re-implementation of ours.
▪ Both runs were scored against the exact mathematical answer, over the interior of the domain.
▪ Neither engine was tuned to match the other.
Ten metres of water, a flat frictionless bed, ten-metre cells, forty seconds of flow, and the three outermost cells at each end trimmed before scoring. Anyone can repeat it.
The result
Engine
Error against the exact answer
Depth at the wall
Verdict
FloodView
0.0317 m
4.532 m
passes
Delft3D FM (Deltares)
0.0349 m
4.515 m
passes
The exact answer (1892)
reference
4.444 m
reference
The two engines agree with each other to 0.0294 metres. Ten metres of water standing behind the wall, forty seconds of flow, and the whole disagreement between them is under three centimetres.
4 / 4 GATES PASSED
and within 3 cm of Delft3D FM
In plain words: the flood predictions here are as accurate as the software governments already trust, and we can show the working. What we do not claim is equally clear — at 30-metre terrain detail, trust the arrival times and the flood boundary; treat any single depth reading as indicative.

## Slide 10
FloodView
PS 26161 · NTRO
HOW IT RUNS, WHAT IS NEW, WHAT COMES NEXT
Packaged to run on one laptop or one server, with no network and no licence.
SMART INDIA
HACKATHON 2026
Everything on the left of this slide already works. The right-hand column is what we build after the hackathon.
10
How it runs
A Browser
Chrome, Firefox or Edge. Nothing to install, nothing to configure.
The Web Service
Answers in about a fifth of a second, even while a simulation is running.
The Simulation Worker
A separate process, so a heavy calculation can never freeze the page.
Local Storage
Results and cached terrain, held on the machine's own disk.
One Container
The whole system packaged so it starts anywhere with a single command.
What is genuinely new here
Verified, not asserted
Cross-checked against a real Deltares kernel running on this machine — demonstrated, not claimed.
A range, not a number
Thirty variations every run, reported as a percentile band around the arrival time.
Bad data is refused
A radar scene below the quality threshold is rejected outright. No synthetic stand-in is ever drawn.
Honest progress
The dashboard reports which member of thirty is solving, rather than a bar that sits still.
Runs with no network
Everything cached after the first fetch, because demo-day connectivity cannot be assumed.
Near-dam 3D detail
Particle physics at the wall, handed off in one direction only — about 600 metres, 15 seconds.
Replaceable parts
Any component can be swapped without touching the others, because dependencies run one way.
Zero licence cost
Every component is open-source. There is nothing to buy before a state can use it.
Where it goes next
DONE
– The flood simulation engine
– The dashboard, eight working tabs
– All four quality gates passing
– The independent Delft3D cross-check
– Thirty-member uncertainty sweep
– Offline-first caching
– Single-command container
NOW
– Impact analysis, final pass
– Near-dam 3D integration polish
– Demo-day rehearsal and fallbacks
NEXT
– Screen all five thousand registered dams
– Hand results to district authorities directly
– Alerts to the phones of people downstream
– A hosted service for states without hardware
– Feed Tier-2 detailed studies where warranted
The framing matters as much as the software. FloodView is a first-pass screening instrument: it tells a state which of its dams deserve a full surveyed study, and in what order. It does not replace that study, and the reports say so on their own face rather than in a footnote.
One laptop is enough to run all of this. Nothing here assumes a data centre, a licence server or a working connection.
None of the last block has been started. It is listed so the boundary between what runs and what is planned stays visible.