## Slide 1: SMART INDIA HACKATHON 2026
FLOODVIEW
Problem Statement ID — 26161
Problem Statement Title — Dam Break Inundation Modelling Using Hydrodynamic Modelling of any River
Theme — Disaster Management
PS Category — Software
Team ID — [from SIH portal]
Team Name — [as registered on portal]

## Slide 2: FloodView
TEAM NAME
Automated dam-break AND landslide-dam inundation modelling: Smoothed Particle Hydrodynamics x Delft3D-class shallow water — quantitatively compared, satellite-validated, zero ground survey
Detailed explanation of the proposed solution
▪ Operator enters a dam or a suspected river blockage — lat/lon, height, gross storage, breach mode. Nothing else.
▪ Pipeline auto-fetches Copernicus GLO-30 DEM (public AWS COGs, no login), CWC NRLD/NRSD dam registers, Sentinel-1 SAR, GHSL and Open Buildings exposure.
▪ Breach hydrograph from Froehlich (2008) / Xu–Zhang (2009) regressions, coupled to weir outflow and reservoir drawdown.
▪ Near field — Smoothed Particle Hydrodynamics resolves the violent, non-hydrostatic breach jet, where depth-averaging is simply invalid.
▪ Far field — Delft3D-class depth-averaged shallow-water finite volume routes the wave tens of km down the valley.
▪ Outputs depth, velocity and arrival-time rasters to a dashboard, plus GeoTIFF / .SHP / .KML.
How it addresses the problem
▪ (i) Both scenario classes — engineered dam break and natural river blockage (Rishi Ganga, Phuktal class) — with loss-and-damage output.
▪ (ii) Pluggable datasets: any DEM, any hydrology source, any AOI.
▪ (iii) Dashboard GUI for model input and tiled output visualisation; .shp / .kml export as specified.
▪ (iv) Google Earth Engine Sentinel-1 SAR module for near-real-time observed flood extent.
▪ (v) Runs live on open Indian data — Tehri (260 m, 3,540 MCM, Koteshwar 13 km downstream) as the engineered case; Chamoli 2021 as the validated natural case.
▪ Automatic by default — coordinates in, decision map out. No hydraulic modeller in the loop, no bathymetric survey, no site access.
Innovation and uniqueness of the solution
▪ The comparison is the product. The PS asks that the two models be compared; we make agreement a measured output — CSI / F1 on wet-cell extent, depth RMSE, arrival-time delta.
▪ Physics-appropriate decomposition, not duplication. SPH is uniform-resolution and cannot span a basin (SPHERIC Grand Challenge 3); depth-averaging cannot resolve a breach jet. Coupled 2D–3D is the direction the review literature itself recommends — we build it.
▪ Validated against a published benchmark, not a pretty animation. Shugar et al. reproduced Chamoli travel times to <5%. That is our target, and the pre/post 2 m DEMs are openly downloadable.
▪ Zero-survey operation — works on transboundary and inaccessible terrain that cannot be instrumented or entered.
▪ Cross-checked against the incumbent: the same reach also runs through HEC-RAS, the tool CWC adopted for DRIP.

## Slide 3: TECHNICAL APPROACH
TEAM NAME
Technologies to be used
Compute Python 3.11 · NumPy · Numba / CuPy (GPU) · xarray · Dask
Near-field solver PySPH — BSD, pip-installable, developed at IIT Bombay; ships dam-break and shallow-water SPH examples with bundled validation data. DualSPHysics (LGPL, CUDA) for GPU scale-up.
Far-field solver Delft3D FM (Deltares, AGPL/GPL) driven by hydromt_delft3dfm · hydrolib-core · dfm_tools; plus an in-house 2D shallow-water finite volume — HLLC Riemann, MUSCL, well-balanced, wetting/drying.
Cross-check HEC-RAS 2D — the CWC / DRIP baseline
Geospatial GDAL · rasterio · geopandas · shapely · simplekml
Earth observation Google Earth Engine Python API · geemap · Sentinel-1 GRD
Data Copernicus GLO-30 (AWS COG) · CWC NRLD 2019 / NRSD 2025 · GHSL · Google Open Buildings · ESA WorldCover · JRC Global Surface Water
Application FastAPI · Celery · React + deck.gl / MapLibre GL
Export GeoTIFF · .SHP · .KML / KMZ
Methodology and process for implementation
1 INPUT — Dam or suspected blockage — lat/lon, height, gross storage, breach mode
2 AUTO-INGEST — Copernicus GLO-30 COGs · CWC NRLD/NRSD · Sentinel-1 · GHSL · WorldCover
3 BREACH HYDROGRAPH — Froehlich 2008 / Xu–Zhang 2009 regressions → weir outflow + reservoir drawdown
4a NEAR FIELD — SPH
Lagrangian, mesh-free. The non-hydrostatic breach jet.
4b FAR FIELD — Delft3D-class 2D SWE
Eulerian finite volume. HLLC + wetting/drying.
5 COMPARE ← the PS's core ask — CSI / F1 on inundation extent · depth RMSE · arrival-time delta
6 LOSS AND DAMAGE — Population, buildings, roads and bridges inside the flood path
7 OUTPUT — Dashboard · arrival-time map · GeoTIFF / .SHP / .KML
8 GEE VALIDATION LOOP — Sentinel-1 SAR observed extent scored against the simulation ↻

## Slide 4: FEASIBILITY AND VIABILITY
TEAM NAME
Analysis of the feasibility of the idea
▪ Every input verified free, open and login-free — Copernicus GLO-30 tiles serve as range-readable COGs from public AWS; Sentinel-1, GHSL and Open Buildings are native Earth Engine assets.
▪ Both named models are genuinely obtainable. PySPH is BSD and `pip install`-able with dam-break cases in the box; Delft3D FM is AGPL/GPL with a maintained Python toolchain.
▪ The far-field solver is textbook numerics — HLLC Riemann solver, MUSCL reconstruction, well-balanced source terms. GPU-accelerated it runs a 30 m reach in minutes on a laptop.
▪ A hard accuracy target already exists: Shugar et al. matched Chamoli travel times to <5%, and the pre- and post-event 2 m DEMs are on Zenodo. Measured discharge 8,200–14,200 m³/s at 15 km.
▪ Scope control — SPH confined to a near-field box, so particle count stays tractable; published real-field cases run 1–4 million particles.
▪ Skills needed: Python, GIS, numerical methods. No proprietary licence, no field survey, no bathymetric campaign.
Potential challenges and risks
▪ Numerical instability at the wet–dry front — negative depths, spurious velocities, mass loss. This fails visibly in a live demo.
▪ SPH does not scale. Uniform resolution is an acknowledged limitation (SPHERIC GC3); it cannot span a basin.
▪ No reservoir bathymetry in any DEM, and GLO-30 is a surface model — it flattens water and puts canopy in the channel.
▪ 30 m cells give 1–2 cells across a Himalayan gorge, so point depths there are fiction, and a cell straddling an embankment lowers the effective crest by metres.
▪ Manning's roughness is uncertain and inundation extent is sensitive to it.
▪ Debris, not clear water. Chamoli was ~80% rock by volume; clear-water physics understates such an event.
▪ Delft3D kernel build risk — Fortran/C++ toolchain, only unofficial Docker images. Liability — a map an officer acts on has consequences.
Strategies for overcoming these challenges
▪ Well-balanced HLLC with hydrostatic reconstruction (Audusse 2004), a depth-positivity limiter and adaptive CFL. Verify against the Ritter analytical solution before touching terrain — correctness first.
▪ Couple, do not choose: SPH near field hands off to shallow-water far field across a coupling boundary — the review literature's own recommendation.
▪ Reservoir volume from NRLD gross storage fitted to a synthetic bathymetric wedge; channel burned in from MERIT Hydro. Report a sensitivity band, never a single line.
▪ Report arrival time and inundation envelope — which 30 m data supports — and label point depths as indicative. Publish a Manning's-n ensemble.
▪ Debris flagged explicitly and approximated with bulked density and roughness. Stated as a caveat, not hidden.
▪ Our own solver carries the live demo; Delft3D FM is the offline reference run, so a build failure cannot break the demonstration.
▪ Every output stamped Tier-1 screening-grade per CWC CDSO_GUD_DS_05, with uncertainty printed on the map itself.

## Slide 5: IMPACT AND BENEFITS
TEAM NAME
204 dead or missing
Chamoli, 7 Feb 2021 — no warning reached anyone
0 deaths
Phuktal, 7 May 2015 — 30–35 Mm³ released, ~3,000 evacuated
2.3 M+ people affected
Kosi, 18 Aug 2008 — breached far below design discharge
The variable between these three rows is not the hydrology. It is whether anyone knew where the water would go, and when.
Potential impact on the target audience
▪ NTRO / HADR planners — scenario generation for dams and natural lakes that cannot be ground-surveyed, including transboundary reaches that are, in ORF's words on the Yarlung Tsangpo, "presently a blind spot for India", where the primary risk is dam failure, not diversion.
▪ NDMA / SDMA / DDMA — depth, extent and arrival time are exactly what an evacuation order needs; .kml drops into the GIS they already run.
▪ CWC / NDSA — a Tier-1 screening layer (CDSO_GUD_DS_05) to triage which dams warrant a full expert study first.
▪ Army / BRO / NDRF — pre-positioning, and deliberate-breach planning of the kind the Army executed at Phuktal in May 2015.
▪ Downstream communities — 29 villages, ~4,000 people and ~50 bridges were at risk at Phuktal alone.
Benefits of the solution
▪ Social — arrival-time maps become lead time, and lead time becomes evacuation. Phuktal: ~3,000 moved, zero deaths.
▪ Economic — zero licence cost against commercial suites, and automation replaces weeks of specialist setup per site.
▪ Environmental — identifies ecosystems and cropland at risk; supports scheduled controlled release instead of emergency release.
▪ Strategic — a no-survey capability for terrain that cannot be physically accessed or instrumented.
▪ Institutional — .shp / .kml at 1:50,000 and 1:10,000 matches CWC EAP map specifications, so results are usable rather than merely viewable.
▪ Scientific — the SPH vs depth-averaged agreement metrics are a publishable contribution, not a repackaged UI.

## Slide 6: RESEARCH AND REFERENCES
TEAM NAME
Problem domain — Indian events and regulation
▪ CWC / CDSO, Guidelines for Mapping Flood Risks Associated with Dams, CDSO_GUD_DS_05 v1.0, Jan 2018 — HEC-RAS adopted for DRIP; Tier 1–3 framework
▪ CWC, Emergency Action Plan guidelines, cwc.gov.in — index maps 1:50,000; detailed maps 1:10,000 at 0.5 m contours
▪ Shugar et al. 2021, Science 373:300–306, doi 10.1126/science.abh4455 — Chamoli rock-and-ice avalanche; 26.9 Mm³; travel times matched to <5%
▪ Rana et al. 2023, Natural Hazards, doi 10.1007/s11069-023-05972-5 — independent HEC-RAS reconstruction of the same event
▪ Sinha 2009, The Great Avulsion of Kosi on 18 August 2008, Current Science 97:429–433
▪ Costa & Schuster 1988, The formation and failure of natural dams, GSA Bulletin
▪ NRSC / ISRO Cartosat-2 monitoring of the Phuktal blockage, Jan–Mar 2015
▪ CWC NRLD 2019 and NRSD 2025 national dam registers (cwc.gov.in)
Numerical methods
▪ Gingold & Monaghan 1977, MNRAS 181:375 — origin of SPH; Lucy 1977, AJ 82:1013
▪ Maranzoni & Tomirotti 2023, 3D Numerical Modelling of Real-Field Dam-Break Flows, Water 15(17):3130, doi 10.3390/w15173130 — recommends coupled 2D–3D
▪ Vacondio et al. 2020, Grand challenges for SPH numerical schemes, Comp. Particle Mech. 8:575–588 — GC3: uniform resolution blocks multiscale use
▪ Vacondio et al. 2011, SPH Modeling of Shallow Flow with Open Boundaries for Practical Flood Simulation, J. Hydraul. Eng.
▪ Prakash, Rothauge & Cleary 2014, Modelling the impact of dam failure scenarios on flood inundation using SPH, Appl. Math. Modelling
▪ Ramachandran et al. 2021, PySPH: A Python-based framework for SPH, ACM TOMS 47(4), doi 10.1145/3460773 (IIT Bombay)
▪ Toro 2001, Shock-Capturing Methods for Free-Surface Shallow Flows, Wiley; Audusse et al. 2004, SIAM J. Sci. Comput.; Liang & Marche 2009, AWR
▪ Froehlich 2008 breach parameters, J. Hydraul. Eng.; Xu & Zhang 2009, JGGE
Software, data and Earth observation
▪ Delft3D — github.com/Deltares/Delft3D (AGPL-3.0 / GPL-3.0); oss.deltares.nl; `hydromt_delft3dfm`, `hydrolib-core`, `dfm_tools`
▪ PySPH — pysph.readthedocs.io (BSD); DualSPHysics — dual.sphysics.org (LGPL, CUDA); GPUSPH (GPLv3)
▪ HEC-RAS — hec.usace.army.mil, incl. official dam-break study guidance
▪ Copernicus DEM GLO-30 — public COGs at s3://copernicus-dem-30m; GEE `COPERNICUS/DEM/GLO30_2024_1`. EGM2008 datum, <4 m vertical (90% LE)
▪ Chamoli validation DEMs — pre-event 2 m zenodo.org/record/4554647, post-event zenodo.org/record/4558692 (CC BY-NC 4.0)
▪ GEE assets — `COPERNICUS/S1_GRD` · `JRC/GSW1_4/GlobalSurfaceWater` · `JRC/GHSL/P2023A/GHS_BUILT_C` · `WorldPop/GP/100m/pop` · `GOOGLE/Research/open-buildings/v3/polygons` · `ESA/WorldCover/v200`
▪ Global Dam Watch v1.0 (CC BY 4.0), doi 10.6084/m9.figshare.25988293 — 41,145 barriers, HydroSHEDS-harmonised, fallback inventory
▪ Malpasset 1959 — the standard real-world dam-break validation case; Ritter/Stoker analytical solution for solver verification
Sources verified Aug 2026. Two dating notes on the PS's reference list: the Phuktal blockage formed 31 Dec 2014 and was breached 7 May 2015; no Nov 2021 Indian river blockage is on record — the likely referent is the 29 Oct 2021 Kameng (Warriyang) sediment event, in which no dam formed. Chamoli was a rock-and-ice avalanche, not a GLOF.